## Slide 1: IRB 57X0 Product and Options
Global Product Management - Large robots
November 2025, version C, Document id:

## Slide 2: Content
IRB 57X0 Intro
IRB 5710 Variants
IRB 5720 Variants
IRB 57X0 Options
01.
02.
03.
04.

## Slide 3: IRB 57X0 Product and Options
Instructions
Customize your sales presentation in RApp 2.0/Showpad today!
Content: All IRB 5700 manipulator variants and options
Target groups: Main: Salespersons and technical product support, Other: Customers
Customer sharing: The content is approved to be shown and shared to a customer.
Instructions: Use the chapters to make your selection of slides to present to your customers. Customize the presentation in RApp 2.0/Showpad, present it and share the link to collect data statistics if needed. Always look for the latest version of the presentation in Rapp 2.0/Showpad.
If you have comments, contact Niko Quiskamp.

## Slide 4: 1. IRB 57X0 Intro

## Slide 5: The IRB 57X0 Range
ABB is expanding its large-size robot portfolio with the IRB 57X0 range, offering faster, more robust, and accurate performance.
Based on a new modular platform, the IRB 57X0’s are offered with the OmniCore controller V250XT and features RobotWare 7.
IRB 57X0’s are ideal for use in material handling, machine tending, and high precision assembly applications in electric vehicle battery production, automotive, and the general industries, but is supporting all industries and business lines.
The robot family is also supporting various process applications. Spotwelding is one key where the robot enables fast and accurate spotwelding with light weight guns. The robots also support high precision applications like Dispense and Laser process

## Slide 6: Shared Features
Protection
  IP 67 protection as standard
Footprint
  Standardized footprint
  Built in features – guide pins for easy replacement
Controller
  Available with OmniCore V250XT
Arm Load
  Additional arm load – Std load 20 kg but built in flexibility to balance between wrist/arm load.
Mounting alternatives
  Floor (std)
  Inverted (Option)
  Angled: (IRB 5710: ≤ 20°, IRB 5720: ≤ 15°) (std)
  Semi-shelf (std)

## Slide 7: Main Benefits
The IRB 57X0 robots are our fastest, most compact and most flexible large robot designed especially for multi-purpose customer applications.
Performance
  Cycle time performance significantly better than IRB 6700
  More compact wrist with same re-orientation capabilities
  Reduced swing radius
  Inverted mounting as option
Modular design
  Shared technical solutions and parts between 90-500 kg payload large robots
  Based on learnings from large installed volume of IRB 6700
  Shared service procedures, spare parts and maintenance intervals
  Shared footprint with same base hole pattern for 90-300kg robots
Options
  Lean ID integrated Dress Pack for best lifetime and off-line programming performance
  Foundry Plus with same high protection as in the IRB 6700 robots

## Slide 8: Shared Features
Semi shelf
The IRB 57X0 is designed to have a better working range for the axis 2 movement, than normal large robots.
This is possible since there is no balancing device.
The axis 2 center is pushed forward, which enables a semi shelf working range (reach below robot foot).
Axis 2 working range: -75° / +145°

## Slide 9: Shared Features
Footprint
  Standardized interface towards the floor, same for the IRB 57X0 as for the IRB 67X0 and 6700.
  Pitch diameter of screw circle 800 mm
  8 holes for M24 screws
  Guiding pins fittings for easier installation
  Footprint 1023 x 724

## Slide 10: Shared Features
Swing radius
  IRB 5710: Front 482 mm / Back 284 mm
  IRB 5720: Front 536 mm / Back 285 mm
Swing radius back
Swing radius front

## Slide 11: Shared Features
Swing radius
  IRB 5710: Front 482 mm / Back 284 mm
  IRB 5720: Front 536 mm / Back 285 mm

## Slide 12: Main Tech Solutions
Drivers
+ Performance
+ Compactness
+ Flexibility
+ Quality / Up-time
+ Energy efficiency
Feature | Value
Motors | 
16-pole motor program | + Compactness, Performance
Brake release board for variable brake voltage | + Compactness, Energy Savings
Electronic box module and interface for brake release | + Modularity, Safety, Usability
Gearboxes | 
Z-series compact gearboxes ax 1-3 & 6 | + Compactness, Performance
Serviceability | 
Unique base variant for inverted mounting | + Serviceability
Standardized lifting and turning tools 90-300 kg | + Modularity, Serviceability
Mechanical Concept | 
No balancing device on axis 2 | + Work range
Inverted mounting available as option for all variants | + Flexibility
Quality | 
Carry-over of IRB 6700 improvements (double seal in motors etc.) | + Quality
Increased static brake torque margin | + Quality
Poka Yoke motor connectors | + Quality
Encapsulated motor ax 6 | + Protection, Serviceability

## Slide 13: Core IRB 57X0 Variants
Model | IRB 5710 | IRB 5710 | IRB 5720 | IRB 5720
Main applications | Spot Welding Material Handling, Dispense, Laser Welding, Assembly (high precision applications) | Material Handling, Dispense, Laser Welding, Assembly (high precision applications) | Spot Welding Material Handling, Dispense, Laser Welding, Assembly (high precision applications) | Spot Welding Material Handling, Dispense, Laser Welding, Assembly (high precision applications)
Configurations | 110 kg / 2.3 m | 90 kg / 2.7 m | 180 kg / 2.6 m | 125 kg / 3.0 m
Options | Lean ID Inverted Foundry Plus | Lean ID Inverted Foundry Plus | Lean ID Inverted Foundry Plus | Lean ID Inverted Foundry Plus

## Slide 14: 2. IRB 5710 Variants

## Slide 15: IRB 5710
IRB 5710 2,3 m
IRB 5710 2,3 m LeanID
IRB 5710 2,7 m
IRB 5710 2,7 m LeanID

## Slide 16: IRB 5710
Options number: 3300-322 – 110kg / 2.3m
Load Diagram
Armload: Upper Arm 20kg
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
50 kg | 0.71374 | 0.70879 | 0.69377 | 0.66814 | 0.63087 | 0.58023 | 0
65 kg | 0.58788 | 0.5836 | 0.5706 | 0.5484 | 0.51612 | 0.47223 | 0
80 kg | 0.4997 | 0.49589 | 0.4843 | 0.46453 | 0.43575 | 0.3966 | 0
100 kg | 0.415 | 0.41163 | 0.40142 | 0.38397 | 0.35857 | 0.32399 | 0
110 kg | 0.3 | 0.29653 | 0.28596 | 0.26778 | 0.24097 | 0.20365 | 0
115 kg | 0.19235 | 0.18821 | 0.17551 | 0.15323 | 0.11913 | 0.068136 | 0

## Slide 17: IRB 5710
Options number: 3300-322 – 110kg / 2.3m
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-180°
  Axis 4 ±300°
  Axis 5 ±130°
  Axis 6 ±360°
Weight
  817kg

## Slide 18: IRB 5710
Options number: 3300-323 – 90kg / 2.7m
Load Diagram
Armload: Upper Arm 20kg
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
40 kg | 0.49471 | 0.49167 | 0.48244 | 0.46677 | 0.44414 | 0.41374 | 0
50 kg | 0.41133 | 0.40866 | 0.40055 | 0.38678 | 0.36689 | 0.34016 | 0
60 kg | 0.35012 | 0.34772 | 0.34043 | 0.32806 | 0.31019 | 0.28615 | 0
70 kg | 0.3028 | 0.30061 | 0.29396 | 0.28267 | 0.26636 | 0.24442 | 0
80 kg | 0.24495 | 0.24303 | 0.23722 | 0.22734 | 0.21307 | 0.19387 | 0
90 kg | 0.19996 | 0.19825 | 0.19308 | 0.1843 | 0.17161 | 0.15455 | 0
95 kg | 0.1043 | 0.10221 | 0.095845 | 0.084866 | 0.068612 | 0.045836 | 0

## Slide 19: IRB 5710
Options number: 3300-323 – 90kg / 2.7m
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-180°
  Axis 4 ±300°
  Axis 5 ±130°
  Axis 6 ±360°
Weight
  813kg

## Slide 20: IRB 5710
Options number: 3300-324 – 90kg / 2.3m LeanID
Load Diagram
Armload: LeanID SW
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
50 kg | 0.61653 | 0.61238 | 0.59984 | 0.57855 | 0.54788 | 0.5068 | 0
60 kg | 0.52113 | 0.51739 | 0.50606 | 0.48684 | 0.45914 | 0.42204 | 0
70 kg | 0.44716 | 0.44373 | 0.43335 | 0.41573 | 0.39035 | 0.35633 | 0
80 kg | 0.37928 | 0.37606 | 0.36633 | 0.34979 | 0.32595 | 0.29397 | 0
90 kg | 0.30013 | 0.29728 | 0.28862 | 0.27393 | 0.25274 | 0.22431 | 0
95 kg | 0.23145 | 0.22858 | 0.21985 | 0.205 | 0.18349 | 0.15443 | 0
100 kg | 0.15004 | 0.14701 | 0.13778 | 0.12198 | 0.098899 | 0.067268 | 0

## Slide 21: IRB 5710
Options number: 3300-324 – 90kg / 2.3m LeanID
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-160°
  Axis 4 ±300°
  Axis 5 ±120°
  Axis 6 ±220°
Weight
  824kg
Limitations & Dependencies
  Requires LeanID Dress Pack

## Slide 22: IRB 5710
Options number: 3300-325 – 70kg / 2.7m LeanID
Load Diagram
Armload: LeanID MH
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
30 kg | 0.60999 | 0.60702 | 0.59805 | 0.5829 | 0.56124 | 0.53254 | 0
40 kg | 0.47021 | 0.4677 | 0.46013 | 0.44732 | 0.42901 | 0.40476 | 0
50 kg | 0.37524 | 0.37304 | 0.36641 | 0.3552 | 0.33916 | 0.31793 | 0
60 kg | 0.28208 | 0.28016 | 0.27438 | 0.26462 | 0.25065 | 0.23214 | 0
70 kg | 0.20035 | 0.19871 | 0.19376 | 0.18539 | 0.17341 | 0.15755 | 0
80 kg | 0.13906 | 0.13762 | 0.13329 | 0.12596 | 0.11549 | 0.10161 | 0
85 kg | 0.1001 | 0.098698 | 0.094472 | 0.087324 | 0.077084 | 0.063482 | 0

## Slide 23: IRB 5710
Options number: 3300-325 – 70kg / 2.7m LeanID
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-160°
  Axis 4 ±300°
  Axis 5 ±120°
  Axis 6 ±220°
Weight
  818kg
Limitations & Dependencies
  Requires LeanID Dress Pack

## Slide 24: 3. IRB 5720 Variants

## Slide 25: IRB 5720
IRB 5720 2,6 m
IRB 5720 2,6 m LeanID
IRB 5710 3,0 m
IRB 5710 3,0 m LeanID

## Slide 26: IRB 5720
Options number: 3300-326 – 180kg / 2.6m
Load Diagram
Armload: Upper Arm 20kg
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
90 kg | 0.72324 | 0.71936 | 0.70764 | 0.68775 | 0.65912 | 0.6208 | 0
110 kg | 0.61136 | 0.60805 | 0.59805 | 0.58108 | 0.55668 | 0.52406 | 0
130 kg | 0.52726 | 0.52437 | 0.51564 | 0.50083 | 0.47953 | 0.4511 | 0
150 kg | 0.46126 | 0.45869 | 0.45093 | 0.43778 | 0.41888 | 0.39367 | 0
165 kg | 0.4202 | 0.41783 | 0.41067 | 0.39853 | 0.3811 | 0.35786 | 0
175 kg | 0.35805 | 0.35567 | 0.34846 | 0.33622 | 0.31858 | 0.29493 | 0
180 kg | 0.3 | 0.29748 | 0.28982 | 0.27677 | 0.25786 | 0.23227 | 0
190 kg | 0.15509 | 0.15183 | 0.14188 | 0.12456 | 0.098509 | 0.060915 | 0

## Slide 27: IRB 5720
Options number: 3300-326 – 180kg / 2.6m
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-180°
  Axis 4 ±300°
  Axis 5 ±130°
  Axis 6 ±360°
Weight
  974kg

## Slide 28: IRB 5720
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
65 kg | 0.59038 | 0.58612 | 0.57316 | 0.55104 | 0.51889 | 0.47518 | 0
80 kg | 0.50195 | 0.49815 | 0.4866 | 0.4669 | 0.43823 | 0.39925 | 0
95 kg | 0.43566 | 0.4322 | 0.42172 | 0.40383 | 0.37779 | 0.34236 | 0
110 kg | 0.36391 | 0.36086 | 0.35161 | 0.3358 | 0.3128 | 0.28151 | 0
125 kg | 0.3002 | 0.29752 | 0.28937 | 0.27547 | 0.25523 | 0.22768 | 0
140 kg | 0.21678 | 0.21417 | 0.20625 | 0.19265 | 0.1727 | 0.14519 | 0
145 kg | 0.15 | 0.14706 | 0.13805 | 0.12243 | 0.099012 | 0.065468 | 0
Options number: 3300-327 – 125kg / 3.0m
Load Diagram
Armload: Upper Arm 20kg

## Slide 29: IRB 5720
Options number: 3300-327 – 125kg / 3.0m
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-180°
  Axis 4 ±300°
  Axis 5 ±130°
  Axis 6 ±360°
Weight
  970kg

## Slide 30: IRB 5720
Options number: 3300-328 – 155kg / 2.6m LeanID
Load Diagram
Armload: LeanID SW
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
75 kg | 0.87155 | 0.86782 | 0.85656 | 0.83755 | 0.81042 | 0.77457 | 0
90 kg | 0.72877 | 0.7255 | 0.71564 | 0.69901 | 0.67526 | 0.6439 | 0
110 kg | 0.56507 | 0.56229 | 0.5539 | 0.53973 | 0.51951 | 0.4928 | 0
125 kg | 0.45574 | 0.4533 | 0.44591 | 0.43344 | 0.41565 | 0.39214 | 0
140 kg | 0.36984 | 0.36766 | 0.36106 | 0.34993 | 0.33404 | 0.31305 | 0
155 kg | 0.3 | 0.29802 | 0.29206 | 0.282 | 0.26764 | 0.24866 | 0
160 kg | 0.20871 | 0.20655 | 0.20002 | 0.18896 | 0.17308 | 0.15192 | 0
165 kg | 0.12295 | 0.12055 | 0.11326 | 0.10085 | 0.082881 | 0.058602 | 0

## Slide 31: IRB 5720
Options number: 3300-328 – 155kg / 2.6m LeanID
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-160°
  Axis 4 ±300°
  Axis 5 ±120°
  Axis 6 ±220°
Weight
  1025kg
Limitations & Dependencies
  Requires LeanID Dress Pack

## Slide 32: IRB 5720
Options number: 3300-329 – 90kg / 3.0m LeanID
Load Diagram
Armload: LeanID SW
Chart: L-distance (m)
| 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
  | 0 | 0 | 0 | 0 | 0 | 0 | 0
40 kg | 0.74622 | 0.74153 | 0.72733 | 0.70324 | 0.66854 | 0.62207 | 0
50 kg | 0.61666 | 0.61251 | 0.59997 | 0.57868 | 0.54802 | 0.50694 | 0
60 kg | 0.52125 | 0.5175 | 0.50618 | 0.48696 | 0.45927 | 0.42217 | 0
70 kg | 0.44727 | 0.44384 | 0.43346 | 0.41585 | 0.39046 | 0.35646 | 0
80 kg | 0.37938 | 0.37616 | 0.36643 | 0.3499 | 0.32606 | 0.29408 | 0
90 kg | 0.30022 | 0.29736 | 0.28871 | 0.27402 | 0.25283 | 0.22441 | 0
100 kg | 0.2369 | 0.23433 | 0.22654 | 0.21332 | 0.19425 | 0.16867 | 0
115 kg | 0.16228 | 0.16004 | 0.15327 | 0.14176 | 0.12517 | 0.10291 | 0

## Slide 33: IRB 5720
Options number: 3300-329 – 90kg / 3.0m LeanID
Working Range
  Axis 1 ±170°
  Axis 2 +145°/-75°
  Axis 3 +70°/-160°
  Axis 4 ±300°
  Axis 5 ±120°
  Axis 6 ±220°
Weight
  1023kg
Limitations & Dependencies
  Requires LeanID Dress Pack

## Slide 34: 4. IRB 57X0 Options

## Slide 35: Base Protection
Options number: 3350-670
Purpose and Value
The manipulators are offered with different protection level. The basic design, option Base 67, is well prepared for normal or tough environment. This includes electrical design following the IP 67 standard and stainless-steel screw used for all add-on parts after painting.
Limitations & Dependencies
—
Ingress Protection
  IP 67

## Slide 36: Foundry Plus 2 Protection
Upgraded paint
UV-resistant polymer covers
Nitrile rubber gaskets
Options number: 3352-10
Purpose and Value
For harsh environments, such as a foundry, the Foundry Plus2 67 option is recommended. This includes extra cable protection, more seals, and coverage for unused connections. The manipulator is finished with a more durable paint and rust preventive.
The main features include:
  Upgraded paint specialized for harsh environments
    Graphite White and Orange standard colors
    Orange color is recommended as it is a risk of color changes over time. The functionality is not affected, only the visual aspect.
  Nickel-phosphorus coating on the tool flange that further reduces corrosion risk in tough environments.
  UV-resistant polymer covers, either PCABS thermo-plastic or PA66 nylon.
  Nitrile rubber gaskets
  Sikaflex sealant
  Stainless steel screws
  Protection plugs for certain unused holes
Limitations & Dependencies
  Option Foundry Plus2 67 requires option Upper Arm Cover 3316-1
  Ingress Protection
  IP 67
Nickel-phosphorus coating

## Slide 37: Foundry Plus 2 – Color Coating
Further clarifications option: 3352-10
Purpose and Value
The robots are available in 2 standard colors (Graphite White and Orange).
For the Foundry applications or in general for extra tough environment the Orange color is recommended as it mitigates the risk of color changes over time better than any other color.

## Slide 38: Foundry Plus 2 – Turning Disc
Further clarifications option: 3352-10
Purpose and Value
In the Foundry Plus 2 Protection option, the turning disc is treated with a nickel-phosphorus coating that further reduces corrosion risk in tough environments.

## Slide 39: Foundry Plus 2 – Covers
Further clarifications option: 3352-10
Purpose and Value
In the Foundry Plus 2 Protection option, additional covers are added to protect hoses/cables and other parts of the manipulator from liquids, hot metal spits and similar

## Slide 40: Foundry Plus 2 – Gaskets
Further clarifications option: 3352-10
Purpose and Value
Gaskets are upgraded to nitrile rubber gaskets to better withstand harsh environment.

## Slide 41: Color Options
Options number: 209-X
Purpose and Value
For our robots, Graphite White is the standard default color, option 209-202. However, the robots are offered in ABB Orange as one additional standard color, option 209-1. Custom-made coloring according to the RAL color systems can be provided.
Limitations & Dependencies
  This is only valid for base manipulators; accessories has a standard color. Normal spare parts are only offered in standard colors

## Slide 42: Foundry Cable Guard
Options number: 3315-1
Purpose and Value
The manipulator could be equipped with additional cable guards for extra tough environmental conditions with as example metals spits, frequent weld spatter. These additional cover will prolong cable lifetime and simplify service/maintenance as the robot are kept cleaner under the covers.
Limitations & Dependencies
  Recommended for 3352-10 Foundry Plus 2 to achieve best protection of the manipulator harness and Dress Pack harness.
  Requires Upper Arm Cover 3316-1

## Slide 43: Upper Arm Cover
Options number: 3316-1
Purpose and Value
The manipulator could be equipped with additional upper arm covers, option 3316-1, for environmental conditions where you want to further seal of the upper arm in wet or dirty conditions. These additional cover will prolong cable lifetime and simplify service/maintenance as the robot are kept cleaner under the covers. The center piece of the cover can be removed if using it together with Dress Pack axis 3-6 harness (routing through the cover).
Made out of UV-resistant PA66 nylon.
Limitations & Dependencies
  Included in option 3352-10 Foundry Plus 2
  Mandatory for option 3315-1 Foundry Cable Guard
  Mandatory for option 3326-xx upper arm Dress Pack options

## Slide 44: Inverted Mounting Position
Options number: 3317-1
Purpose and Value
The manipulator could be placed inverted to add more flexibility in layout design. The robot is prepared in production for inverted mounting.
Limitations & Dependencies
  Not possible together with AbsAcc Floor mounted

## Slide 45: Forklift Device
Options number: 3318-1 on base, 3318-2 on frame
Purpose and Value
The manipulator can be delivered with forklift devices. These devices allow a truck with forks to be used when the manipulator must be moved. Instructions on how to mount the devices is included in the kit.
There are two different alternatives.
  Forklift loops placed on the base, option 3318-1, which allows for a low lifting point.
  Forklift rails placed on the frame, option 3318-2, which allows a more balanced lifting point. This could be used together with special tool to invert a robot.
Limitations & Dependencies
  3318-1 on base not compatible with 3317-1 Inverted
  To be removed after installation / use
  Preparations and consideration at use specified in product manuals
  Delivered on pallets including bolts
  Tools to invert a robot to be coordinated with ABB after market team
Option 3318-1 on base
Option 3318-2 on frame

## Slide 46: 7th Axis Resolver Connection
Options number: 3322-1 On base, 3322-2 In servo Dress Pack
Purpose and Value
The manipulator could be prepared to support an additional servo motor drive, e.g., to enable track motion or servo tools. The option includes connection of one extra resolver channel beside the 6 axis that are used in the basic robot.
Used to connect an external axis resolver feedback from the motor to the control system.
There are two different alternatives.
  Resolver signal for one additional motor are routed to the foot of the robot, option 3322-1
  Resolver signals for one additional motor are routed via the Dress Pack to the tool, option 3322-2
Limitations & Dependencies
  Only one extra motor possible
  Option 3322-2 In servo Dress Pack is required for servo options of Dress Pack base-axis 3
Option 3322-2 In servo Dress Pack
Option 3322-1 On base

## Slide 47: Additional drive units • Robot held servo tool • Stationary servo tool
Options number 3062-1, 3068-1, 3068-2, 3206-x
  OmniCore V250XT controller is available with up to 3 ADU (additional Drive Unit) and up to 6 ADU with V400XT for use with robot held OR stationary servo motor. Typically for Spotwelding, servo gripper, stationary transport or other.
Purpose & value
Only valid for V250XT and V400XT
Option uses only one ADU
This option is available for the following robots: IRB 2600, 4600, 57X0, 6650S, 6700, 67X0, 67X0S, 6760, 460, 660, 7600, 77X0
Limitations & Dependencies
MDU
M03:06/11
M08:06
ADU 1
M03:07
M06:09
M04:03/02
Included in servo-dress pack selection
Matching legacy dress pack with single wire-solution (low power)
Floor cable – single motor, low power
SMB
Servo tool
ADU 1
OmniCore V250XT
MDU
M03:06/11
M08:06
ADU 1
M03:07
M06:09
M04:03/02
Floor cable – single motor, low power
Requires “connection on base” on the manipulator
OmniCore V250XT
SMB
Servo tool
ADU 1

## Slide 48: Limited Working Range Axis 1
Options number: 3323-1
Purpose and Value
Used to mechanically restrict the motion range of axis 1.
The manipulator can be equipped with adjustable stops which mechanically limit the working range on axis 1. The mechanical stops are delivered alongside the robot. The stops can be mounted in 15-degree increments. Assembly instructions are covered in the product manual.
Limitations & Dependencies
  Not compatible with 3324-1 Extended working range

## Slide 49: Extended Working Range Axis 1
Options number: 3324-1
Purpose and Value
The working range of the manipulator can be increased on axis one by removing the mechanical stop, increasing the range to ±220°. This allows the user to reach critical points behind the robot.
The option Extended work range enables an extension of the working range for axis one, through a software configuration. With this option installed, the working range can exceed the standard range limited by the mechanical stop on axis one. The working range shall be limited through the option SafeMove.
The mechanical stop are assembled at delivery and could be removed once other safety measures has been performed. Removal process are stated in the product manual.
Limitations & Dependencies
  Not compatible with 3317-1 Inverted
  Not compatible with 3325-xx Dress Pack SpotWelding
  Requires 3043-X SafeMove
X

## Slide 50: Motor Cooling Fans
Options number: 3320-1 for axis 1, 3321-1 for axis 2
Purpose and Value
The manipulator could be delivered with fans for axis one and two. This is to handle cases with high duty cycle and/or high surrounding temperature.
There are three different alternatives:
Cooling fans axis 1, option 3320-1, placed directly on the axis 1 motor base
Cooling fans axis 2 option 3321-1, placed directly on the axis 2 on robot frame
To be used to avoid overheating of motor and gear in applications with intensive motion (high average speed and/or high average torque and/or short wait time) of axis one and two.
Limitations & Dependencies
  IP 54 valid for cooling fan
  “Gearbox Heat Prediction” tool is available in RobotStudio to determine the need of fans
  Not compatible with 3352-10 Foundry Plus 2 67

## Slide 51: Dress Pack - Overview
Concepts
Purpose and Value
The IRB 57X0 robots can be equipped with different Dress Packs. The Dress Packs are well integrated into the robot system with focus on long life length and large working range and accurate off-line simulations. ​
​
The Dress Pack is designed as a complete system including mainly 5 main building blocks with connection points in between: ​
  Preparations for the Dress Pack inside the robot controller cabinet​.
  Floor cables from cabinet to base of robot​.
  Lower arm Dress Pack from base of robot to rear part of the upper arm (axis 3).​
  Upper arm Dress Pack from rear part of upper arm (axis 3) to the tool flange (axis 6).​
  Connections kits to simplify local made interface solutions (available for base, axis 3 and axis 6).​
​
The upper arm Dress Pack consists of two design solutions, LeanID (LID) and MH3. The LeanID solution is available for both Material Handling and Spotwelding. The MH3 solution also supports only Material Handling. ​ The LeanID solution could also be supplied as "Empty Conduit". This to support local made "customized" Dress Pack content.​
The different Dress Pack solutions are supported by offering complete CAD models to download to support simulation and simplify the steps from virtual environment to actual programs. ​
​More customer values could be found in other sales document.​
​ Customer benefits
  The Dress Pack is modularly built with the aim to offer a complete solution.
  It is possible to buy separate sections.
  More customer values could be found in other sales document.

## Slide 52: Dress Pack - Overview
Details
Design details
Further details on the design and option structure will be found in the coming slides.
The main difference between LeanID and MH3 is that LeanID is guided across the axis 6 center of rotation by utilizing a process turning disc (PTD) instead of the standard turning disc. This allows for a controlled and predictable motion pattern of the Dress Pack.
IRB 5710-70/2.7 LeanID with its long upper arm contains a smaller diameter protective conduit (Ø52mm) at axis 5-6 compared to IRB 5710-90/2.3 LID (Ø70mm) due to a smaller “process turning disc”.

## Slide 53: Overview Dress Pack - Controller and Manipulator options
Connection to Dress Package, Principal structure – Material Handling
Connection in controller
Floor cable
Manipulator Dress Pack MH
Electronic HW and RW
Cable to LAN
3060-1
Cable to WAN
Parallel signals
3201-x
Base to Ax3
3325-11 Parallel
3325-13 Ethernet
3325-14 CC-Link
3325-15 EtherCat
Base to Ax3
Ax3 to Ax6
MH3:
3326-11 Parallel
LID MH:
3326-31 Parallel
Ax3 to Ax6
MH3:
3326-13 Ethernet
3326-14 CC-Link
3326-15 EtherCat
LID MH:
3326-33 Ethernet
3326-34 CC-Link
3326-35 EtherCat
Parallel signals
3055-2
3202-x Ethernet
3205-x CC-Link
3210-x EtherCat
Parallel signals + Industrial Ethernet fieldbus
3020-x PROFInet
3024-x EtherNet/IP
3066-x CC-Link IE
3075-x EtherCat

## Slide 54: Overview Dress Pack - Controller and Manipulator options
Connection to Dress Package, Principal structure – Spot Welding
Electronic HW and RW
Connection in controller
Floor cable
Manipulator Dress Pack SW
Cable to LAN
3060-1
Cable to WAN
Parallel signals
3201-x
Base to Ax3
3325-61 Parallel
3325-63 Ethernet
3325-64 CC-Link
3325-65 EtherCat
Base to Ax3
Ax3 to Ax6
3326-61 Parallel
Ax3 to Ax6
LID:
3326-63 Ethernet
3326-64 CC-Link
3326-65 EtherCat
Parallel signals
3055-2
Parallel signals + Industrial Ethernet fieldbus
3020-x PROFInet
3024-x EtherNet/IP
3066-x CC-Link IE
3075-x EtherCat
3202-x Ethernet
3205-x CC-Link
3210-x EtherCat

## Slide 55: Dress Pack - base-axis 3
Options number: 3325-xx
MH
SW
Purpose and value
Dress Pack harness from the base up to axis 3 are routed in different ways depending on choosing Material Handling (MH) or SpotWelding (SW). MH is routed through the Lower Arm whilst the SW is routed outside the same. SW has also a protective conduit stretching from the Frame up to the Arm housing.
Options number
  3325-11 MH Parallel
  3325-13 MH Ethernet
  3325-14 MH CC-Link
  3325-15 MH EtherCat
  3325-61 SW Parallel-Servo
  3325-63 SW Ethernet-Servo
  3325-64 SW CC-Link-Servo
  3325-65 SW EtherCat-Servo
Limitations & Dependencies
  3325-61, -63, -64 & -65 (SW Dress Pack) not compatible with option 3324-1 Extended Working Range Axis 1.
  3325-61, -63, -64 & -65 (SW Dress Pack) only optional if Floor cable is chosen.
Recommendations
  Complement with corresponding Floor cable.
  Complement with compatible Dress Pack axis 3-6, Empty Conduit or Connection kit
  Complement with option 3352-10 Foundry Plus2 67 and 3315-1 Foundry Cable Guard to protect exposed sections of the Dress Pack harness.

## Slide 56: Dress Pack – base-axis 3 – Material Handling
Further clarification option: 3325-xx
Purpose and value
Connector plates and connectors for the harness is included when choosing a “Dress Pack – base-axis 3”, both at the base and at the axis 3 interface. Here is an explanation of the different connections and when they are used.
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | Servo Feedback (when option 3322-1 On base is selected) | MH/SW
D | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
E | PROC 1 (1/2” Hose) | MH/SW
F | FE (Functional Earth, when EtherNet communication is selected) | MH/SW
Base
Axis 3
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
D | PROC 1 (1/2” Hose) | MH/SW
E | FE (Functional Earth, when EtherNet communication is selected) | MH/SW
Base
Axis 3

## Slide 57: Dress Pack – axis 6 – Material Handling
Further clarification option: 3326-xx
Purpose and value
Connectors for external Dress Pack (MH3) and LeanID is included when choosing an upper arm Dress Pack. Here is an explanation of the connections for axis 6 and when they are used.
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
D | PROC 1 (1/2” Hose) | MH/SW
E | FE (Functional Earth, when Ethernet communication is selected) | MH/SW
Axis 6

## Slide 58: Dress Pack – base-axis 3 – Spot Welding
Further clarification option: 3325-xx
Purpose and value
Connector plates and connectors for the harness is included when choosing a “Dress Pack – base-axis 3”, both at the base and at the axis 3 interface. Here is an explanation of the different connections and when they are used.
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | Servo Feedback (when Servo is selected) Servo Power (when Servo is selected) | MH/SW
D | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
E | Weld Power | SW
F | PROC 1 (1/2” Hose) | MH/SW
G | PROC 2-4 (1/2” Hose) | SW
H | FE (Functional Earth, when EtherNet communication is selected) | MH/SW
Base
Axis 3
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | Servo Feedback (when Servo is selected) | MH/SW
D | Servo Power (when Servo is selected) | MH/SW
E | Weld Power | SW
F | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
G | PROC 1 (1/2” Hose) | MH/SW
H | PROC 2-4 (1/2” Hose) | SW
I | FE (Functional Earth, when EtherNet communication is selected) | MH/SW
Base
Axis 3

## Slide 59: Dress Pack – axis 6 – Spot Welding
Further clarification option: 3326-xx
Purpose and value
Connectors for external Dress Pack (MH3) and LeanID is included when choosing an upper arm Dress Pack. Here is an explanation of the connections for axis 6 and when they are used.
Pos | Description | Application
A | Customer Power | MH/SW
B | Customer Signal | MH/SW
C | ETHERNET (M12 connector, when Ethernet communication is selected) | MH/SW
D | PROC 1 (1/2” Hose) | MH/SW
E | FE (Functional Earth, when Ethernet communication is selected) | MH/SW
F | Servo Power (when Servo is selected) | SW
G | Servo Feedback (when Servo is selected) | MH/SW
H | Weld Power (3x) | SW
I, J, K | PROC 2-4 (1/2” Hose) | MH/SW
Axis 6

## Slide 60: Dress Pack - axis 3-6
Options number: 3326-xx
Conduit
PTD
Options number
  3326-11 MH3 Parallel
  3326-13 MH3 Ethernet
  3326-14 MH3 CC-Link
  3326-15 MH3 EtherCat
  3326-30 MH LID Empty Conduit
  3326-31 MH LID Parallel
  3326-33 MH LID Ethernet
  3326-34 MH LID CC-Link
  3326-35 MH LID EtherCat
  3326-50 SW LID Empty Conduit
  3326-61 SW LID Parallel-Servo
  3326-63 SW LID Ethernet-Servo
  3326-64 SW LID CC-Link-Servo
  3326-65 SW LID EtherCat-Servo
Limitations & Dependencies
Standard variant of manipulator mandatory for MH3 options.
LID variant of manipulator mandatory for SW/MH LID (incl. Empty conduit) options.
Smaller conduit size for “MH3” (Ø52).
Smaller conduit size for “MH LID” on variant IRB 5710-70/2.7 LID.
SW / MH LID
IRB 5710-90/2.3 LID
IRB 5720-155/2.6 LID
IRB 5720-90/3.0 LID
IRB 5710-110/2.3
IRB 5710-90/2.7
IRB 5720-180/2.6
IRB 5720-125/3.0
MH3
MH LID
IRB 5710-70/2.7 LID

## Slide 61: Dress Pack – MH/SW LID Empty Conduit
Options number: 3326-xx
Purpose and Value
The IRB 57X0 robots can be equipped with the LeanID (LID) Empty Conduit option. This is an option enabling the customer to route their own cables and hoses through the protected tubes and guidings of a LeanID upper arm.
The protective conduit has a diameter of 70mm, except for the IRB 5710-70/2.7 LID variant which has Ø52.
Options number
  3326-30 MH LID Empty Conduit
  3326-50 SW LID Empty Conduit
Limitations & Dependencies
  LID variant of manipulator mandatory for both options on LID Empty Conduit.
  Smaller conduit size for “MH LID Empty Conduit” on variant IRB 5710-70/2.7 LID
  Dress Pack base – axis 3 mandatory
Hose and cable retainer
(incl. fillers)
Ø70
Ø52

## Slide 62: Connector Kits Base
Options number: 333X-X
Purpose and value
If the customer wish to make an own floor cable for the Dress Pack, a connection kit is available. The kit contains the connectors that will fit to the corresponding ones on the base.
Options number
3330-2 CP/CS bus, Proc 1 base
3331-1 Weld Proc 2-4 base
3332-1 FB7 on base
Limitations & Dependencies
-
Base
3330-2 CP/CS bus, Proc 1 base
3332-1 FB7 on base
3331-1 Weld Proc 2-4 base

## Slide 63: Connector Kits Axis 3
Options number: 3333-X
Purpose and value
If the customer wish to make an own upper arm cable for the Dress Pack (axis 3-6), a connection kit is available. The kit contains the connectors that will fit to the corresponding ones on the axis 3 connection plate.
Options number
3333-2 CP/CS bus, Proc 1 axis3
3333-3 CP/CS Proc1, Servo & FB
Limitations & Dependencies
-
Axis 3
3333-2 CP/CS bus, Proc 1 axis 3
3333-3 CP/CS Proc1, Servo & FB

## Slide 64: Connector Kits Axis 6
Options number: 333X-X
Purpose and value
A connection kit is available for customers to facilitate the connection between axis 6 and the customer’s tool. The kit contains the connectors that will fit to the corresponding ones on the base.
Options number
  3334-2 CP/CS bus, Proc 1 axis6
  3334-3 CP/CS Proc1, Servo & FB
  3335-1 Weld Proc 2-4 axis 6
Limitations & Dependencies
-
Axis 6
3334-2 CP/CS bus, Proc 1 axis6
3334-3 CP/CS Proc1, Servo & FB
3335-1 Weld Proc 2-4 axis 6